## Slide 1
Evaluation on the thermal behavior of urban surfaces using an energy balance model
Fanxing Zeng, Naiping Gao
School of Mechanical Engineering, Tongji University

## Slide 2
Outline
Motivation
Introduction
  Town Energy Balance model (TEB)
  Meteorological forcing data
Results
  Annual temperature cycle
  Diurnal temperature cycle
Conclusions

## Slide 3
What is the first step to understand
the nature of urban microclimate?
Motivation
Introduction
Results
Conclusions
Urban surface temperature as a diagnostic parameter to describe the urban microclimate
Micrometeorological model
Penman-Monteith equation
Computational Fluid Dynamic
（CFD）
Urban Canopy Model（UCM）
CFD & UCM
Notes: Before we go deep into the main topic, I want to talk about why we have chosen urban canopy mode to analyze thermal behaviors of urban area , or we say a lumped energy model model. So when I ask you :…? You may come out with different answers, and the answers will be very much depend on your research background and your research purposes? While in terms of the scales you are studying, if we use a tree as a scale indicator, the methods will all fall into the range of these three categories, namely ….. …… …… we found it very tricky to take into account both thermal and solar radiation into the model even in CFD, so in this stage, we used a energy balance model called teb to learn the urban surface temperature evoluation.

## Slide 4
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions
Town Energy Balance model (TEB)
An urban surface parameterization developed by Valéry Masson et al, Météo France
Purpose and design of TEB
  Urban surface sensible and latent heat flux, momentum and radiation exchange for atmospheric models
TEB is not designed for
  Simulations at the scale of one single building
  Details of the wind and temperature fields in the street canyons (vs. CFD methods)
  Details inside the buildings

## Slide 5
Purpose and design of TEB
  Urban surface sensible and latent heat flux, momentum and radiation exchange for atmospheric models
TEB is not designed for
  Simulations at the scale of one single building
  Details of the wind and temperature fields in the street canyons (vs. CFD methods)
  Details inside the buildings
An urban surface parameterization developed by Valéry Masson et al, Météo France
  TEB model
  Meteorological forcing data
Town Energy Balance model (TEB)
Motivation
Introduction
Results
Conclusions

## Slide 6
TEB assumptions on urban morphology
Buildings oriented along street canyons with
length >> width
Homogeneous urban morphology
  Identical urban canyons
Any road orientation is possible and all exist with the same possibility
  No discretization is performed on orientation
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 7
Radiation modification due to buildings
Mean direct solar fluxes received in a canyon perpendicular to sun direction
Net longwave radiation is computed with one re-emission considered. The sky view factor for road and wall are needed.
Solar zenith angle
Roof
Road
Wall
（Masson 2000）
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 8
Calculation of temperature, humidity and wind speed inside the street canyon
Aerodynamic resistances Modified after Masson 2000
Where different surfaces (i.e. roof, wall and road) are normalized with the subscript to represent either R, r, or w.
Energy terms are net solar radiation, net infrared radiation, sensible heat flux, latent heat flux and conduction heat between the surface layer and the inner layer, respectively
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 9
Surface cover fractions (building, road, vegetation)
Urban geometry
  Building height
  Wall to horizontal area ratio
Architectural characteristics
  Albedo, emissivity, thickness, thermal conductivity
  capacity of roofs, walls, road, floor and mass
Required input data featuring the urban area
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 10
Urban parameters input of TEB model for Toulouse city center
Inputs-urban geometry
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 11
Inputs-thermal property
Surfaces discretization-5 layers
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 12
Required meteorological forcing data
Air temperature and specific humidity
Wind speed and direction
Direct and diffuse downwelling solar radiation
Downwelling infra-red radiation
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 13
The CAPITOUL campaign
Canopy and Aerosol Particles Interaction in TOulouse Urban Layer
  Observations in Toulouse, February 2004 to March 2005
  Urban surface energy balance measured at meteorological mast
City center of Toulouse
  Homogeneous urban morphology
  ~20m-high red brick buildings
  Vegetation is rare
  Not much industry
  TEB model
  Meteorological forcing data
Motivation
Introduction
Results
Conclusions

## Slide 14
Annual temperature cycle
The smooth curves derived from fourth order polynomial fit to the TEB mean temperatures
Averaged road temperature
in the city center:
[2.8,28.4 ℃] Low value
Road vs. Canyon air temperature profile:
-Phase displacement
-Amplitude attenuation
20/02/2004-28/02/2005
TEB time step was fixed to 5min and outputs are averaged over 30min period.
Motivation
Introduction
Results
Conclusions

## Slide 15
  Roof albedo:0.40
  Road albedo: 0.08
Motivation
Introduction
Results
Conclusions
Annual temperature cycle

## Slide 16
Motivation
Introduction
Results
Conclusions
Annual temperature cycle

## Slide 17
Diurnal temperature cycle
Mar. 8 to Mar. 14, 2004
Jul. 25 to Jul. 31, 2004
Oct. 15 to Oct. 21, 2004
Jan. 15 to Jan. 21, 2004
Motivation
Introduction
Results
Conclusions
Ensemble averaged weekly data

## Slide 18
Ensemble-averaged diurnal temperature cycle for seven sunny days in different seasons
TEB evaluation:
One-month Measurement*
in Fall and winter with infra-red thermometers for a selected set of walls, roads and roofs with different orientations and aspect ratios.
 | Fall (15/10/04-15/11/04) |  | Winter (15/01/04-15/02/04) | 
 | Bias (K) | RMSD (K) | Bias (K) | RMSD (K)
Roof | 1.0 | 2.1 | 1.2 | 2.2
Road | -1.4 | 1.6 | -2.2 | 2.4
Wall | 0.8 | 0.9 | 0.0 | 0.5
* Raw data from Pigeon 2008
All temperature
vary strongly
in summer
Diurnal temperature validation
Motivation
Introduction
Results
Conclusions

## Slide 19
Conclusions
Annual mean temperature cycle of urban surfaces and canyon air indicate a time lag phenomenon between air and canyon surfaces.
The surface temperature varies strongly(24℃ for roof) in a daily cycle during summer time but an even larger variation could be discovered if we enlarge the evaluation period to an annual cycle(26℃ for road).
In the comparison of the diurnal and annual cycle, the temporal and spatial scale is found to be the cause of different temperature evolution pattern for urban surfaces.
Motivation
Introduction
Results
Conclusions

## Slide 20
TEB model is a useful tool to reveal the thermal response of urban canyon surfaces if the forcing data is accessible.
However, it’s hard to validate the simulation results -classical techniques can only be applied on a limited extent (e.g. only few observational sites in the city, shorter time series)
Achilles’ heel of impact studies using TEB: garbage in garbage out?
Further discussion
Motivation
Introduction
Results
Conclusions

## Slide 21
Thank you
solarzeng@hotmail.com