## Slide 1: The Town Energy Balance (TEB): An urban surface parametrization developed at Météo France
2017-04-21 课题组讨论会
曾繁兴

## Slide 2: Outline
Motivation for the development of the Town Energy Balance (TEB)
Fundamentals of TEB
Meteorological forcing data
Applications for urban climate studies
The CAPITOUL campaign and simulation results

## Slide 3: Motivation for the development of the Town Energy Balance (TEB)

## Slide 4
Surface energy, water and momentum balance depends on land use type
Figure De Munck (2013)

## Slide 5
Surface energy balance impacts local climate
Differences between urban and rural climate – (Nocturnal) air temperature higher in urban area (UHI) – Relative humidity lower in urban area – Absolute humidity can be higher in urban area – Wind speed lower in urban area – Enhancement/suppression of clouds and precipitation possible
Figure De Munck (2013)
Nocturnal (2 AM) air temperature observed in Toulouse on July 4 2004 during the CAPITOUL campaign (Masson et al., 2008)

## Slide 6
Purpose and design of TEB – Urban surface energy, water, momentum balance for atmospheric models – Sensible and latent heat flux, momentum and radiation exchange – The scale of application is an urban district, not single buildings – Numerical integration must be a lot faster than for atmospheric model TEB is not designed for – Simulations at the scale of one single building – Details of the wind and temperature fields in the street canyons – Details inside the buildings
What is TEB made for?

## Slide 7: Fundamentals of TEB

## Slide 8
TEB architecture

## Slide 10: Meteorological forcing data

## Slide 12
Required meteorological forcing data – Air temperature and specific humidity – Wind speed and direction – Air pressure – Direct and diffuse downwelling solar radiation – Downwelling infra-red radiation – Rain and snow fall rate

## Slide 13: The CAPITOUL campaign and simulation results

## Slide 14
The CAPITOUL campaign -Canopy and Aerosol Particles Interaction in TOulouse Urban Layer
-Conducted over the city of Toulouse, France to quantify thermal dynamical processes and surface-atmosphere interaction within urban boundary layer
-during February 2004 to March 2005.
-The observational network includes a city centre tower equipped with a complete surface energy balance measurement system and 20 stations over the Toulouse agglomeration

## Slide 15
Schematic view of the central site Masson, V.,Gomes, L. et al.2008

## Slide 16
Map of the temperature stations network
Grégoire Pigeon and Valéry Masson, 2009

## Slide 19
Annual temperature cycle from TEB simulation

## Slide 20
Ensemble-averaged temperature cycle for seven days （2004.7.25-7.31）under anticyclone weather

## Slide 21
Conclusions
-For the analysis of urban microclimate, the main weakness of energy balance models is that the velocity field is not directly modelled. On the other hand, in CFD, velocity field can be coupled with temperature field. Therefore, CFD has the potential to be an important tool for the deterministic analysis of urban microclimate and consequently for the analysis of adaptation measures in building and urban scale.
-After defining the objective of study, the degree of complexity included in the models and computational cost of the case are the principal constraints in a reliable urban microclimate simulation which need to be properly dealt with in the future study.

## Slide 22: The end
谢谢各位！